## Slide 1: Results on the zz boards scans
Aiwu Zhang
02/29/2016

## Slide 2
Scanned two zigzag boards on a 10 cm GEM detector, one board has 30 strips and the other one has 48 strips, along phi (across strips) as well as along R (in the strip direction). Also collected some data with mini-GEM config plus COMPASS r/o board for reference.
Electronics: BNL preamp + Strucks 3300/3301 ADCs were used. Total 24 channels. Noise is very small (overall < 1 ADC count) and not saturating the signals. Every channel is calibrated with zz boards connected. Thanks to Bob, Martin and Mike Phipps for helping me with the setup and software.
For the zz boards scans, either 1- or 2-strip signals were observed for X ray, there were few 3,4-strip signals for other source (cosmic ray).
General information

## Slide 3
Analyses – Trying to get a good start point
X
Y
At the beginning of each scan, the x-ray gun is set to motor’s absolute position. The distance from this absolute point to the board corner can be measured (with a ±0.5 mm precision), so that roughly, I can locate on the zigzag board the region that was scanned.
The measured distances from absolute point to the corner are 79.0 mm in X and 75.7 mm in Y.

## Slide 4
Analyses – Cluster Builder
Mike Phipps has a data analysis software package (based on C++ & ROOT) which unpacks raw data and writes TTrees. Then further analysis can be done based on TTrees.
It is important that a cluster is well defined and reconstructed. In Mike’s package, two cuts are applied: (1) N sigma threshold cut (N=5); (2) avg charge cut event by event, avg charge calculation is based on 3-strip events, in case of <3-strip events, this cut is useless. The results are (1) many real cluster multiplicity = 1 events are excluded; (2) strip multiplicity (or cluster size) turns to be bigger (this is why cluster size 4~5 in the summer data.).
To overcome the issue, the 2nd cut is changed to: cut away a strip-hit where the max. charge < N*5*sigma, N=4. This is the same as to say: S/N ratio to be bigger than 5N (N=4).
S/N>4
Clust. Multi. > 1;
Clust. Size = 4.
Clust. Multi. = 1;
Clust. Size = 2.

## Slide 5
Results – scan on ZZ_30 board, along phi (across strips)
Centroid (in phi) vs. X (Y=53.2 mm)
Cluster size vs. X (Y=53.2 mm)
Cluster charge vs. X (Y=53.2 mm)
Scanned 3.7 mm along X, step 0.1 mm
Note the source came from
a collimator of 50 um (X) by 8 mm (Y)
Almost all events have cluster size < 2
(except cosmic signals)
0.5 mm

## Slide 6
Results – scan on ZZ_30 board, along phi (across strips)
Centroid (in phi) vs. X (Y=53.2 mm)
8mm
Ratio of copper area in the 8mm*0.05mm region.
(measured with FAB 3000 software.)

## Slide 7
Results – scan on ZZ_30 board, along R (across zigzag tips)
Centroid (in phi) vs. Y (X=51 mm)
Cluster size vs. Y (X=51 mm)
Cluster charge vs. Y (X=51 mm)
Y
X

## Slide 8
Results – scan on ZZ_30 board, along R (across zigzag tips)
Centroid (in phi) vs. Y (X=51 mm)
Y
2 mm
8 mm
Ratio of copper area in the 8mm*0.05mm region.
(measured with FAB 3000 software.)

## Slide 9
Results – scan on ZZ_48 board, along phi (across strips)
Centroid (in phi) vs. X (Y=53.2 mm)
Cluster size vs. X (Y=53.2 mm)
Cluster charge vs. X (Y=53.2 mm)
Scanned 4.9 mm along X, step 0.1 mm
Note the source came from
a collimator of 50 um (X) by 8 mm (Y)
Almost all events have cluster size < 2
(except cosmic signals)

## Slide 10
Results – scan on ZZ_48 board, along phi (across strips)
Centroid (in phi) vs. X (Y=53.2 mm)
Cluster size vs. X (Y=53.2 mm)
Almost all events have cluster size < 2
(except cosmic signals)
Ratio of copper area in the 8mm*0.05mm region.
(measured with FAB 3000 software.)
8 mm

## Slide 11
Results – scan on ZZ_48 board, along phi (across strips)
Centroid (in phi) vs. X (Y=53.2 mm)
Y axes on the right plots:
Centroid [mm] – X ray position [mm]
The plots on the right are similar to residual vs X ray position ! Note that X ray position is not smeared.
(need to translate X ray position to the origin of the board from the current motor origin.).
Contains clusterSize >1 evts only
Mean centroid from evts with all clusterSize

## Slide 12
Results – scan on ZZ_48 board, along phi (across strips)
Centroid (in phi) vs. X (Y=53.2 mm)
Residual vs.
(for 5 runs in the linear region)
Residual vs.
(for 7 runs in the linear region)
beam test data
The function shows different band for different run, but overall the bands are in the same region as compare to the beam test data. The reasons could be (1) beam test data actually covers 2~3 cm along phi (across ~10 strips), this averages out to be one wide band as seen; (2) when making the new functions, x ray position (which is needed is residual calculation) is a fixed number for each run.

## Slide 13
Results – scan on ZZ_48 board, along R (across zigzag tips)
Centroid (in phi) vs. Y (X=51 mm)
Cluster size vs. Y (X=51 mm)
Cluster charge vs. Y (X=51 mm)
Y
X

## Slide 14
Results – scan on ZZ_48 board, along R (across zigzag tips)
Centroid (in phi) vs. Y (X=51 mm)
Cluster size vs. Y (X=51 mm)
Ratio of copper area in the 8mm*0.05mm region.
(measured with FAB 3000 software.)

## Slide 15
Results – HV scan with Fe-55 on ZZ_48 board, at X=51, Y=55.2
Centroid
Cluster size (mean)
Cluster charge
Position scans on the zz boards were done at HV=3380V (I should have mentioned it earlier).
Here in the HV scan, with an Fe-55 source putting roughly at the middle of the detector, centroid mean tends to be flat after 3350 V.

## Slide 16
Summary of the ZZ scans
Cluster size (or strip multiplicity) is < 3 for most of the events (from the observation during data taking, cluster size > 3 events are only from cosmic ray signals).
For the ZZ30 and ZZ48 boards, nonlinear response is seen again. It is confirmed that a linear region is between two strips from tip to tip, and beyond that region response is nonlinear. Nonlinear response along strips is small, and it can be partly explained by the copper occupancy ratio fluctuation.
For the ZZ48 board, if count only cluster size = 2 evts, spatial resolution is estimated to be about (120±10) μrad in the entire linear region (by subtracting in quadrature the rms of 50um (estimate) due to the collimator).

## Slide 17: Backup slides following

## Slide 18
Results – scan on ZZ_30 board, along phi (across strips)
Run 1309
Run 1322
Run 1335
Strip number 14
Strip number 14
Strip number 15
Strip number 15
There are two peaks in the centroid distribution when X ray is !! The left peak comes from events whose charge on left strip is bigger than on right strip, similar as to the right peak!
Cluster Size = 2
Bigger charge on left strip
Bigger charge on right strip
Centroid
Run 1322
Cluster Size >= 1
Two peak not happened in the ZZ48 data

## Slide 19
Results – scan on compass r/o board with mini drift GEM
Mini-drift: 15.63/1.7/1.69/2.16 mm; strip width in X (Y) is 0.32 mm (0.12 mm).
Each direction has 12 channels.
Scan along Y, centroid in strip number vs. Y coordinate [X=51 mm]
Scan along X, centroid in strip number vs. X coordinate [Y=53.2 mm]
Cluster size
Cluster size

## Slide 20
Results – scan on compass r/o board with mini drift GEM
Scan along Y, centroid in strip number measured by X strips
Scan along X, centroid in strip number measured by Y strips
Strip width in X (0.32 mm) is larger, it turns out that centroid measured in X direction is not flat, it peaks at center of each strip and right in between neighboring strips.
Strip width in Y (0.12 mm) is small enough, so the centroid measured in Y direction is much flatter.
Centroid measured by X strips in a run in the scan-X-runs
Centroid measured by Y strips in a run in the scan-Y-runs
A hot channel
Run 110
Run 400
12 channels (4.8 mm) in X all fired
(note collimator is 8 mm)
12 channels (4.8 mm) in Y all fired
(note collimator is 8 mm)
Run 110
Run 400

## Slide 21
Results – scan on compass r/o board with mini drift GEM
Run 110
Run 400
Run 400
In the scans along Y, strips in X DON’T measure good charge spectra. Not sure why
Charge in X
Charge in Y
Total Charge
In the scans along X, strips in X measure reasonable charge spectra.
Charge in X
Charge in Y
Total Charge